## Slide 1: 第三次新人週報
工號:1200106
姓名:黃劭宸
到職日:109/03/30

## Slide 2: GSD 200 SOURCE HEAD
DISMANTLING
ASSEMBLE
ISOLATION TEST
引用自SAMUEL - 山姆爾的GSD 200 SOURCE HEAD Maintenance Guideline

## Slide 3
DISMANTLING
OF COMPONENTS

## Slide 4
移除四根RETAIN PIN
移除ARC SLIT
鬆開螺絲讓CATHODE WIRE 跟CATHODE SUPPORT PLATE分離
移除CERAMIC CATHODE TUBE
1
2
3
4

## Slide 5
鬆開固定MOUNTING BLOCK的兩顆螺絲
移除MOUNTING BLOCK ASSEMBLY
MOUNTING BLOCK RETAINER SCREW
鬆開四根SHOULDER SCREW
3
4
1
2
5
6
7

## Slide 6
移除ARC CHAMBER
1. ARC CHAMBER 2. SPACER SCREW
3. SHOULDER SCREWS
移除REPELLER
移除BASE, SIDE, REPELLER and FILAMENT
PLATES LINER
1
2
3
8
9
10

## Slide 7
把CATHODE, CATHODE REPELLER 和 FILAMENT分解開來
CLEAN THE COMPONENTS IN SAND BLAST AREA
AIR SPRAY THE COMPONENTS TO REMOVE SAND RESIDUE
…WIPE CLEAN WITH IPA
拆下的零件帶去噴沙
11
12

## Slide 8
ASSEMBLE
OF COMPONENTS

## Slide 9
清理好的SOURCE BODY
安裝CERAMIC SPACER
安裝SHOULDER SCREW SPRING
TOP / MOUNTING SLOT
1
2

## Slide 10
安裝ARC CHAMBER
安裝四個SHOULDER SCREW 暫時先不鎖緊
安裝BALL JOINT, GAS SPRING, and SKT JOINT 在GAS LINE上
接著可以鎖緊四個SHOULDER SCREWS 確保ARC CHAMBER 跟SKT JOINT 沒間隙 以避免氣體外洩
MUST BE NO GAP
3
4
5
6

## Slide 11
安裝套在SUPPRESION LINE外的CERAMIC CATHODE TUBE
SUPPRESION LINE
7

## Slide 12
把MOUNTING BLOCK INSULATOR 、CATHODE SUPPORT PLATE、FILAMENT CLAMP 組裝在一起
CATHODE SUPPORT PLATE
MOUNTING BLOCK INSULATOR
8

## Slide 13
把FILAMENT CLAMP撐開以夾住ELS FILAMENT
把CATHODE裝到CATHODE SUPPORT PLATE上
CATHODE碰到ELS FILAMENT 後 轉出3/4圈
9
10

## Slide 14
把CATHODE REPELLER裝到CATHODE上
暫時不鎖緊
11

## Slide 15
確認FILAMENT 在CATHODE WALL內且與四周等距離沒有接觸
標記CATHODE SUPPORT PLATE 與CATHODE 位子(FILAMENT跟CATHODE剛好碰到時)
轉出CATHODE 3/4圈
這時可以將CATHODE REPELLER鎖緊
12
13
14
15

## Slide 16
將MOUNTING BLOCK 部件安裝到 ARC CHAMBER上
螺絲將MOUNTING BLOCK SCREW RETAINER、ARC CHAMBER 、MOUNTING BLOCK 三者鎖在一起固定
HERE!
HERE!
16
17

## Slide 17
確保螺絲都有鎖緊
確保CATHODE在ARC CHAMBER WALL裡置中位子
安裝BASE PLATE LINER
用鏡子檢查或是看兩側與上面間距是否一致即可知道位置是否置中
確保螺絲都有鎖緊
18
19
20

## Slide 18
安裝FILAMENT PLATE LINER
安裝REPELLER END PLATE LINER
組裝REPELLER 部件
安裝SIDE PLATES LINER
21
22
23
24

## Slide 19
確保REPELLER有鎖緊
確保CONNECTION兩端都有鎖緊固定好
安裝CATHODE CONNECTOR跟WIRE
重複確認ARC CHAMBER裡的零件是否有裝好
25
26
27
28

## Slide 20: ISOLATION TEST

## Slide 21
FILAMENT需要導通
SUPPRESSION LINE跟CATHODE SUPPORT PLATE需要導通
REPELLER跟ARC CHAMBER需要絕緣
FILAMENT LINE跟SOURCE BODY需要絕緣
1
2
3
4

## Slide 22
SOURCE BODY跟CATHODE SUPPORT PLATE需要絕緣
ARC CHAMBER跟CATHODE SUPPORT PLATE需要絕緣
CAHODE SUPPORT PLATE跟FILAMENT CLAMP需要絕緣
5
6
7

## Slide 23
安裝ARC SLIT
用RETAINER PIN固定ARC SLIT
29
30

## Slide 24
用IPA清理O-RING 溝槽
簽上組裝人名字跟組裝日期
確認O-RING無損傷以免影響漏率
用IPA清理並塗上VACUUM GREASE裝上
31
32
33