## Slide 1
VL-800 Auto load/unload 設定

## Slide 2
等待時間、速度參數
Speed
S1: manual S2: low S3: medium
S4: high
S5 : motion 1 and 4 load
S6 : motion 2 and 5 load
S7 : motion 3 and 6 load
S8 : motion 1 and 4 unload
S9 : motion 2 and 5 unload
S10 : motion 3 and 6 unload
Time
T1: reserved
T2: reserved
T3 : motions 1 and 4 wait time load
T4 : motions 2 and 5 wait time load
T5 : motions 3 and 6 wait time load
T6 : motions 1 and 4 wait time unload
T7 : motions 2 and 5 wait time unload
T8 : motions 3 and 6 wait time unload
T9 : time between the closing of DS-SWG axis and
the elevating of DS-UD axis
T10 : reserve

## Slide 3
Load
Motion 1: S5、T3
Motion 2: S6、T4
Motion 3: S7、T5
Motion 4: S5、T3
Motion 5: S6、T4
Motion 6: S7、T5
Motion 7: output a load end signal
Unload
Motion 1: S8、T6
Motion 2: S9、T7
Motion 3: S10、T8
Motion 4: S8、T6
Motion 5: S9、T7
Motion 6: S10、T8
Motion 7: output an unload end signal
參數總結

## Slide 4
Motion 1~3 Load (cap保持在上方版本)
初始位置
BE_UD: P4
HA_ROT: P1 DS_UD: P2 DS_SWG: P2 GC_LOK: P1
BE_UD to P1 at speed 4 (high speed)
DS_SWG to P1 (closed)
Wait at T9 DS-UD to P1 (up)
BC_LOK to P2 (free)
BE_ROT to P1 (P2) HA_ROT to P2
BE_UD to P2 at speed 2 (low speed)
HA_ROT to P3
Wait at T3
DS_UD to P2 (down)
DS_SWG to P2 (open)
BE_UD to P4
Motion 4~6 Load
初始位置
BE_UD: P1
HA_ROT: P1 DS_UD: P1 DS_SWG: P1 GC_LOK: P1
BC_LOK to P2 (free)
BE_ROT to P1 (P2)
HA_ROT to P2
BE_UD to P2
HA_ROT to P3
Wait at T3
DS_UD to P2 (down)
DS_SWG to P2 (open)
BE-UD to P8

## Slide 5
Motion 1~3 Unload (cap保持在上方版本)
初始位置
BE_UD: P4
HA_ROT: P3 DS_UD: P2 DS_SWG: P2 GC_LOK: P2
BE_UD to P2 at speed 8
DS_SWG to P1 (closed)
Wait at T9 DS-UD to P1 (up)
BE_ROT to P1 (P2)
Wait at T6
HA_ROT to P2
BE_UD to P1
HA_ROT to P1
DS_UD to P2 (down)
DS_SWG to P2 (open) BE_UD to P4 at speed 4 (high speed)
Motion 4~6 Unload
初始位置
BE_UD: P4
HA_ROT: P3 DS_UD: P2 DS_SWG: P2 GC_LOK: P2
BE_UD to P2 at speed 8
DS_SWG to P1 (closed)
Wait at T9 DS-UD to P1 (up)
BE_ROT to P1 (P2)
Wait at T6
HA_ROT to P2
BE_UD to P1
HA_ROT to P1
BC_LOK to P2 (locked)